## Slide 1
Repair Sharing
[P8P67 LE]: Halt at B2
The Initial Problem Analysis:
1 : Visually check MB slot for damage. Check front and back of the board for line breaks.
2: Check SX1 if it has 32.768 KHz or not. Check PU16 PIN2 +3VSB and OR1 PIN1 +3VSB_ATX are normal.
3: After plugging CPU and power on, VGA card has no display at B2 code.
4: Definition and Type of no display:
A. B2 is about detecting PCIE function
B. Some data would show it’s detecting others bus of SB, like: SIO LPC
Repair process
MB Type | L1 Problem Description | Needed materials situation | L2 Problem Description | Signal | Position Number
P8P67 LE | Halt at B2 |  |  | U3U1 hot | U3U1
Measure VCORE and GFX
Visually Check
CPU Frequency Signal H_CPURST# S_CPUPWRGD
SB Power
+3V, 3VSB, 3VSB_ADV
+1.05V
1.8VSFR
VCCIO
3_3P3_DAV_FB
VCCDMI_PLL_PCH
VCCA_DPLLB
VCCA_DPLLA
CK_100M_DMI

## Slide 2
SB Frequency
25MHz
CK_14M_PCH
CK_96M_PCH
CK_100M_PCH
CK_100M_DMI
CK_100M_USB3
CK_100M_EATA
CK_100M_SATA
CK_100M_LAN
SB Others Signals
O_PWROK
S_PLTRST#
PCIE Device
Check SATA (mavell 9172, if fail, it’s possible to halt at “94”)
USB3, LAN…
Try to remove PCIE device chipset to confirm
When removing U3U1(USB3 chipset), it’s very hot. Try to exchange a new one to solve this case.
If it still fail
SIO Condition
Check SIO Power +BAT +3V +3VAB_ATX
Check SIO Frequency 33M 48M
Check PG and RST signals ASUS_EN O_PWROK S_PLTRST#
Check LPC signals S_LAD[0:3] LFRAME
Check power detect pin impedance (voltage divider resistor) O_VCOREREFEIN O_12VIN O_5VIN VCOREIN
Problem: B2 caused from “SIO 12V sense pin floating”.
Check SIO PIN O_+12VIN has 0V (normal voltage is about 1V)，check O_+12VIN voltage divider resistor and find OR23 is OPEN. Try to exchange OR23 to solve this case.